MODEL: HMCI25TB

CONVECTION MICROWAVE OVEN

Microwave Oven   Owner's Manual

# PRECAUTIONS TO AVOID POSSIBLE EXPOSURE TO EXCESSIVE MICROWAVE ENERGY

Do not attempt to operate this oven with the door open since open door operation can result in harmful exposure to microwave energy. It is important not to defeat or tamper with the safety interlocks. Do not place any object between the oven front face and the door or allow soil or cleaner residue to accumulate on sealing surfaces. Do not operate the oven if it is damaged. It is particularly important that the oven door close properly and that there is no damage to the Door (bent), Hinges and latches (broken or loosened), Door seals and sealing surfaces. The oven should not be adjusted or repaired by anyone except properly qualified service personnel.

CONTENTS

PRECAUTIONS TO AVOID POSSIBLE EXPOSURE TO EXCESSIVE MICROWAVE ENERGY	1

SPECIFICATIONS	2

BEFORE YOU CALL FOR SERVICE	2

INSTALLATION	2

GROUNDING INSTRUCTIONS	3

RADIO INTERFERENCE	3

IMPORTANT SAFETY INSTRUCTIONS	3

MICROWAVE COOKING PRINCIPLES	6

UTENSILS GUIDE	6

PART NAMES	7

CONTROL PANEL	8

HOW TO SET THE OVEN CONTROLS	9

SETTING THE CLOCK	9

MICROWAVE	9

GRILL	9

MICRO+GRILL	9

CONVECTION	10

MICROWAVE +CONVECTION	10

SPEED DEFROST	10

WEIGHT DEFROST	11

MENU COOK	11

PRESET FUNCTION	15

ECO MODE	15

SLIENCE	15

CHILD PROOF LOCK	15

CLEANING AND CARE	16

# SPECIFICATIONS

| Power Consumption: | 230V~50Hz, 1400W (Microwave) |
| --- | --- |
|  | 1950W (Convection) |
|  | 1000W (Grill) |
| Rated Microwave Output: | 900W |
| Operation Frequency: | 2450MHz |
| Outside Dimensions: | 405mm(W)×483mm(D)×292mm(H) |
| Oven Cavity Dimensions: | 340mm(W)×344mm(D)×220mm(H) |
| Oven Capacity: | 25Litres |
| Cooking Uniformity: | Turntable System |
| Net Weight: | Approx. 16kg |

# BEFORE YOU CALL FOR SERVICE

If the oven fails to operate:

- Check to ensure that the oven is plugged in securely. If it is not, remove the plug from the outlet, wait 10 seconds, and plug it in again securely.

- Check for a blown circuit fuse or a tripped main circuit breaker. If these seem to be operating properly, test the outlet with another appliance.

- Check to ensure that the control panel is programmed correctly and the timer is set.

Check to ensure that the door is securely closed engaging the door safety lock system. Otherwise, the microwave energy will not flow into the oven.

IF NONE OF THE ABOVE RECTIFIES THE SITUATION, THEN CONTACT A QUALIFIED TECHNICIAN. DO NOT TRY TO ADJUST OR REPAIR THE OVEN YOURSELF.

# INSTALLATION

- Make sure that all the packing materials are removed from the inside of the door.

- WARNING: Check the oven for any damage, such as misaligned or bent door, damaged door seals and sealing surface, broken or loose door hinges and latches and dents inside the cavity or on the door. If there is any damage, do not operate the oven and contact qualified service personnel.

- This microwave oven must be placed on a flat, stable surface to hold its weight and the heaviest food likely to be cooked in the oven.

- Do not place the oven where heat, moisture, or high humidity are generated, or near combustible materials.

- For correct operation, the oven must have sufficient airflow. Allow 20cm of space above the oven, 10cm at back and 5cm at both sides. Do not cover or block any openings on the appliance. Do not remove feet.

- Do not operate the oven without glass tray, roller support, and shaft in their proper positions.

- Make sure that the power supply cord is undamaged and does not run under the oven or over any hot or sharp surface.

- The socket must be readily accessible so that it can be easily unplugged in an emergency.

- Do not use the oven outdoors.

# GROUNDING INSTRUCTIONS

This appliance must be grounded. This oven is equipped with a cord having a grounding wire with a grounding plug. It must be plugged into a wall receptacle that is properly installed and grounded. In the event of an electrical short circuit, grounding reduces risk of electric shock by providing an escape wire for the electric current. It is recommended that a separate circuit serving only the oven be provided. Using a high voltage is dangerous and may result in a fire or other accident causing oven damage.

WARNING Improper use of the grounding plug can result in a risk of electric shock.

Note

- If you have any questions about the grounding or electrical instructions, consult a qualified electrician or service person.

- Neither the manufacturer nor the dealer can accept any liability for damage to the oven or personal injury resulting from failure to observe the electrical connection procedures.

The wires in this cable main are colored in accordance with the following code:

Green and Yellow = EARTH

Blue = NEUTRAL

Brown = LIVE

# RADIO INTERFERENCE

Operation of the microwave oven can cause interference to your radio, TV, or similar equipment.

When there is interference, it may be reduced or eliminated by taking the following measures:

- Clean door and sealing surface of the oven.

- Reorient the receiving antenna of radio or television.

- Relocate the microwave oven with respect to the receiver.

- Move the microwave oven away from the receiver.

- Plug the microwave oven into a different outlet so that microwave oven and receiver are on different branch circuits.

# IMPORTANT SAFETY INSTRUCTIONS

When using electrical appliance basic safety precautions should be followed, including the following:

WARNING: To reduce the risk of burns, electric shock, fire, injury to persons or exposure to excessive microwave energy:

- Read all instructions before using the appliance.

Use this appliance only for its intended use as described in this manual. Do not use corrosive chemicals or vapors in this appliance. This type of oven is specifically designed to heat, cook or dry food. It is not designed for industrial or laboratory use.

Do not operate the oven when empty.

Do not operate this appliance if it has a damaged cord or plug, if it is not working properly or if it has been damaged or dropped. If the supply cord is damaged, it must be replaced by the manufacturer or its service agent or a similarly qualified person in order to avoid a hazard.

Warning: When the appliance is operated in the combination mode, children should only use the oven under adult supervision due to the temperatures generated.

WARNING: Only allow children to use the oven without supervision when adequate instructions have been given so that the child is able to use the oven in a safe way and understands the hazards of improper use.

To reduce the risk of fire in the oven cavity:

- When heating food in plastic or paper container, keep an eye on the oven due to the possibility of ignition;

- Remove wire twist-ties from paper or plastic bags before placing bag in oven.

- If smoke is observed, switch off or unplug the appliance and keep the door closed in order to stifle any flames.

- Do not use the cavity for storage purposes. Do not leave paper products, cooking utensils or food in the cavity when not in use.

WARNING: Liquid or other food must not be heated in sealed containers since they are liable to explode.

Microwave heating of beverage can result in delayed eruptive boiling, therefore care has to be taken when handling the container.

Do not fry food in the oven. Hot oil can damage oven parts and utensils and even result in skin burns.

Eggs in their shell and whole hard-boiled eggs should not be heated in microwave ovens since they may explode even after microwave heating has ended.

Pierce foods with heavy skins such as potatoes, whole squashes, apples and chestnuts before cooking.

The contents of feeding bottles and baby jars should be stirred or shaken and the temperature should be checked before serving in order to avoid burns.

Cooking utensils may become hot because of heat transferred from the heated food. Potholders may be needed to handle the utensil.

Utensils should be checked to ensure that they are suitable for use in microwave oven.

WARNING: It is hazardous for anyone other than a trained person to carry out any service or repair operation which involves the removal of any cover which gives protection against exposure to microwave energy.

This product is a Group 2 Class B ISM equipment. The definition of Group 2 which contains all ISM (Industrial, Scientific and Medical) equipment in which radio-frequency energy is intentionally generated and/or used in the form of electromagnetic radiation for the treatment of material, and spark erosion equipment. For Class B equipment is equipment suitable for use in domestic establishments and in establishments directly connected to a low voltage power supply network which supplies buildings used for domestic purpose.

This appliance is not intended for use by persons (including children) with reduced physical, sensory or mental capabilities, or lack of experience and knowledge, unless they have been given supervision or instruction concerning use of the appliance by a person responsible for their safety.

Children should be supervised to ensure that they do not play with the appliance.

The microwave oven is only used in freestanding.

WARNING: Do not install oven over a range cooktop or other heat-producing appliance. if installed could be damaged and the warranty would be avoid .

The accessible surface may be hot during operation.

The microwave oven shall not be placed in a cabinet.

The door or the outer surface may get hot when the appliance is operating.

The temperature of accessible surfaces may be high when the appliance is operating.

The appliance shall be placed against a wall.

Appliance is not to be used by children or persons with reduced physical, sensory or mental capabilities, or lack of experience and knowledge, unless they have been given supervision or instruction

Children being supervised not to play with appliance

WARNING: If the door or door seals are damaged, the oven must not be operated until it has been repaired by a competent person

The instructions shall state that appliances are not intended to be operated by means of an external timer or separate remote-control system.

The microwave oven is for household use only and not for commercial use.

Never remove the distance holder in the back or on the sides, as it ensures a minimum distance from the wall for air circulation.

Please secure the turn table before you move the appliance to avoid damages.

Caution: It is dangerous to repair or maintain the appliance by no other than a specialist because under these circumstances the cover have to be removed which assures protection against microwave radiation. This applies to changing the power cord or the lighting as well. Send the appliance in these cases to our service centre.

The microwave oven is intended for defrosting, cooking and steaming of food only.

Use gloves if you remove any heated food.

Caution! Steam will escape, when opening lids or wrapping foil.

This appliance can be used by children aged from 8 years and above and persons with reduced physical, sensory or mental capabilities or lack of experience and knowledge if they have been given supervision or instruction concerning use of the appliance in a safe way and understand the hazards involved. Children shall not play with the appliance. Cleaning and user maintenance shall not be made by children unless they are aged from 8 years and above and supervised.

If smoke is emitted, switch off or unplug the appliance and keep the door closed in order to stifle.

# MICROWAVE COOKING PRINCIPLES

- Arrange food carefully. Place thickest areas towards outside of dish.

- Watch cooking time. Cook for the shortest amount of time indicated and add more as needed. Food severely overcooked can smoke or ignite.

- Cover foods while cooking. Covers prevent spattering and help foods to cook evenly.

- Turn foods over once during microwaving to speed cooking of such foods as chicken and hamburgers. Large items like roasts must be turned over at least once.

# UTENSILS GUIDE

Rearrange foods such as meatballs halfway through cooking both from top to bottom and from the center of the dish to the outside.

- The ideal material for a microwave utensil is transparent to microwave, it allows energy to pass through the container and heat the food.

- Microwave can not penetrate metal, so metal utensils or dishes with metallic trim should not be used.

- Do not use recycled paper products when microwave cooking, as they may contain small metal fragments which may cause sparks and/or fires.

- Round /oval dishes rather than square/oblong ones are recommend, as food in corners tends to overcook.

- Narrow strips of aluminum foil may be used to prevent overcooking of exposed areas. But be careful don’t use too much and keep a distance of 1 inch (2.54cm) between foil and cavity.

The list below is a general guide to help you select the correct utensils.

| Cookware | Microwave | Grill | Convection | Combination* |
| --- | --- | --- | --- | --- |
| Heat–Resistant Glass | Yes | Yes | Yes | Yes |
| Non Heat–Resistant Glass | No | No | No | No |
| Heat–Resistant Ceramics | Yes | Yes | Yes | Yes |
| Microwave–Safe Plastic Dish | Yes | No | No | No |
| Kitchen Paper | Yes | No | No | No |
| Metal Tray | No | Yes | Yes | No |
| Metal Rack | No | Yes | Yes | No |
| Aluminum Foil & Foil Container | No | Yes | Yes | No |

- Combination: applicable for both "microwave+ grill", and "microwave+ convection" cooking.

# PART NAMES

Door Safety Lock System

Oven Window

Roller Ring

Shaft

Door Release Button

Control Panel

Wave Guide (Please do not remove the mica plate covering the wave guide)

Glass Tray

Grill Heater

Baking Plate

# CONTROL PANEL

(Please also see the following pages for more detail)

DISPLAY SCREEN

Cooking time, power, indicators and present time are displayed.

POWER LEVEL

Press to select microwave power level.

CLOCK

Press to set the clock or to set food weight.

GRILL

Press to set a grill cooking program.

MICRO+GRILL

Press to set a combination cooking program.

DEFROST

Press to set defrosted program.

CONVECTION

Press to program convection temperature.

MICRO+CONVECTION

Press to select one of four combination cooking settings.

PRESET

Use to set preset function.

+ -

Press to set cooking time 、cooking weight

or select auto-menu.

START

Press to start cooking program or set quick start cooking program.

STOP

Touch to stop cooking program or clear all previous settings before cooking starts.

# HOW TO SET THE OVEN CONTROLS

SETTING THE CLOCK

Suppose you want to set the clock time 8:30.

- Press CLOCK button..

- Press “+ -” pad until the hour digit “8” is displayed.

- Press START button.

- Press “+ -” pad until the “8:30” is displayed.

- Press START button to confirm.

Note: This is a 24-hour clock.

QUICK START

Use this feature to program the oven to microwave food at 100% power conveniently.

In standby mode, press START in quick succession to set the cooking time. Also you can add cook time during cooking. The maximum cooking time is 10 minutes. The oven will start working automatically.

MICROWAVE

Microwave cooking allows you to customize cooking power and time. The longest cooking time is 95 minutes.

- Press POWER LEVEL once and touch “+ -” pad repeatedly to select cooking power.

- Press START pad to confirm the power.

- Press “+ -” pad to enter cook time.

- Press START.

Note: You can check the power level during cooking by pressing POWER LEVEL.

GRILL

It is also suitable for hot sandwiches and au gratin dishes. The longest cooking time is 95 minutes.

Suppose you want to program grill cooking for 12 minutes.

- Press GRILL button.

- Press “+ -” pad to 12:00.

- Press START.

MICRO+GRILL

This feature allows you to combine grill and microwave cooking on two different settings. The longest cooking time is 95 minutes. During cooking, you can see the programmed setting by pressing MICRO+GRILL.

COMBINATION

COMBINATION 1: 30% of time for microwave cooking, 70% for grill cooking.

COMBINATION 2: 55% of time for microwave cooking, 45% for grill cooking.

Suppose you want to set combination 2 cooking for 12 minutes.

- Press MICRO+GRILL button once.

- Press “+ -” pad to select combination 2, “Co-2” will display.

- Press START to confirm

- Press “+ -” pad to enter cook time.

- Press START.

CONVECTION

During convection cooking, hot air is circulated throughout the oven cavity to make crisp foods quickly and evenly. This oven can be programmed for ten different cooking temperatures (110℃~200℃). The longest cooking time is 95 minutes. Press CONVECTION button to set convection temperature.

Suppose you want to cook at 180℃ for 40 minutes.

- Press CONVECTION once and touch “+ -” pad repeatedly to select cooking temperature.

- Press START pad to confirm the power.

- Press “+ -” pad to enter cook time.

- Press START.

MICROWAVE +CONVECTION

This oven has four pre-programmed settings that make it easy to cook with both convection heat and microwave automatically. The longest cooking time is 95 minutes. During cooking, you can press MICRO+CONVECTION to check power level.

Press MICRO+CONVECTION repeatedly to select convection temperature:

|  | Oven temperature(℃) |
| --- | --- |
| COMB1 | 200 |
| COMB2 | 170 |
| COMB3 | 140 |
| COMB4 | 110 |

Suppose you want to bake food for 24 minutes on 170℃.

- Press MICRO+CONVECTION once and touch “+ -” pad repeatedly to select cooking temperature.

- Press START pad to confirm the power.

- Press “+ -” pad to enter cook time.

- Press START.

Note: You can check the temperature during cooking by pressing MICRO+CONVECTION.

SPEED DEFROST

- In standby, press DEFROST pad once, “0：00”will display.

- Press “+ -” pad to enter defrost time.

- Press START.

WEIGHT DEFROST

- In standby, press DEFROST pad twice, “0g”will display.

- Press “+ -” pad to enter defrost time.

- Press START.

MENU COOK

For food or the following cooking mode, it is not necessary to program the time and the cooking power. It is sufficient to indicate the type of food that you want to cook as well as the weight of this food.

- In standby, press pad once, “A-1”will display.

- Press “+ -” pad to enter select the desired menu.

- Press START.

- Press “+ -” pad to enter select the desired submenu.

- Press START.

- Press “+ -” pad to enter weight or number of servings.

- Press START.

Auto Cook Code

| Menu | weight/pcs | Power | Timing |
| --- | --- | --- | --- |
| A-1 BAKING |  |  |  |
| b-1 Savoury pie | 1pcs(in crispy plate) | CO1+P0+CO2+P80(Grill) | 2:00+stop & take out the base and stuff+7:00+3:00 |
| b-2 Yeast | 500g | P10(MWO) | 10:00 |
|  | 1000g | P10(MWO) | 15:00 |
| b-3 Bread | 500g | MWO/Convection 180°+ Convection | 15:00+3:00 |
|  | 1000g | MWO/Convection 180°+ Convection | 19:00+3:00 |
| b-4 Wholemeal pizza | 400g-450g | MWO/Convection 180°+ P80(Grill) | 12:00+3:00 |
| A-2 FISH |  |  |  |
| b-1 Slice of swordfish | 180g-200g | CO2 +P0+CO2+P80(Grill) | 2:30+stop and flip+2:30+2:00 |
|  | 360g-400g | CO2 +P0+CO2+P80(Grill) | 3:30+stop and flip+3:30+3:00 |
| b-2 Fillet of salmon | 180g-200g | CO2 +P0+CO2+P80(Grill) | 2:30+stop and flip+2:30+2:00 |
|  | 360g-400g | CO2 +P0+CO2+P80(Grill) | 3:30+stop and flip+3:30+3:00 |
| b-3 Bream | 250g | CO2 +P0+CO2+P80(Grill) | 3:00+stop and flip+3:00+2:00 |
|  | 500g | CO2 +P0+CO2+P80(Grill) | 4:30+stop and flip+4:30+3:00 |
| b-4 Shrimps | 200g | CO2 +P0+CO2+P80(Grill) | 1:30+stop and flip+1:30+2:00 |
|  | 400g | CO2 +P0+CO2+P80(Grill) | 2:30+stop and flip+2:30+3:00 |
| A-3 VEGETABLES |  |  |  |
| b-1 Spinach | 250g | P100(MWO) | 2:30 |
|  | 500g | P100(MWO) | 3:00 |
| b-2 Sliced carrots | 250g | P100(MWO)+P0+P80(MWO) | 3:00+stop and mix+2:30 |
|  | 500g | P100(MWO)+P0+P80(MWO) | 4:00+stop and mix+4:00 |
| b-3 Broccoli | 250g | P100(MWO)+P0+ P80(MWO) | 3:00+stop and mix+2:00 |
|  | 500g | P100(MWO)+P0+ P80(MWO) | 4:00+stop and mix+3:30 |
| b-4 Vegetable soup | 250g | P100(MWO)+P0+ P100(MWO) | 5:00+stop and mix+5:00 |
|  | 500g | P100(MWO)+P0+ P100(MWO) | 6:00+stop and mix+6:00 |
| A-4 MEAT/EGGS |  |  |  |
| b-1 Chicken breasts | 200g | CO2+P0+ CO2+P80(Grill) | 3:00+stop and mix+3:00+2:00 |
|  | 400g | CO2+P0+ CO2+P80(Grill) | 4:00+stop and mix+4:00+3:00 |
| b-2 Tenderloin veal | 500 g | CO1+P0+CO2+P80(Grill) | 5:30+stop and flip+5:30+4:00 |
|  | 1kg | CO1+P0+CO2+P80(Grill) | 8:00+stop and flip+8:00+5:00 |
| b-3 Poached eggs | 1 PCS | P100(MWO)+P0+ P100(MWO) | 1:00+0:10+0:20 |
| b-4 Scrambled eggs | 2-4PCS | P100(MWO)+P0+P60(MWO)+P0+P60(MWO) | 0:40+stop and stir+0:30+ stop and stir+0:20+ stir |
| A-5 HEALTHY |  |  |  |
| b-1 Natural yogurt | 900g+750ml milk | P100(MWO)+P0+ P100(MWO) | 1:00+ stop and add some yogurt+0:15 |
| b-2 Soaked legumes | 250g+1kg water | P100(MWO) | 7:00 |
|  | 500g+2kg water | P100(MWO) | 7:00 |
| b-3 Dried food | 250g | P100(MWO)+P0+ P100(MWO) | 3:00+0:30+2:00 |
| b-4 Porridge | 40g+240ml milk | P100(MWO) +P0(beep to stir)+P80(MWO) | 2:00+stop and stir+ 1:00 |
| A-6 PASTA/CEREALS |  |  |  |
| b-1 Wholemeal pasta | 33g+67g water | P100(MWO)+P0+ P80(MWO) | 5:00+add salt and mix+5:00 |
|  | 67g+133g water | P100(MWO)+P0+ P80(MWO) | 5:00+stop and mix+5:30 |
|  | 100g+200g water | P100(MWO)+P0+ P80(MWO) | 5:00+stop and mix +6:00 |
|  | 133g+267g water | P100(MWO)+P0+ P80(MWO) | 5:00+stop and mix+6:30 |
| b-2 Wholemeal rice | 25g rice+75g water | P100(MWO)+P0+P80(MWO) | 20:00+stop and stir+6:00 |
|  | 50g rice+150g water | P100(MWO)+P0+P80(MWO) | 20:00+stop and stir+8:00 |
|  | 75g rice+225g water | P100(MWO)+P0+P80(MWO) | 20:00+stop and stir+10:00 |
|  | 100g rice+300g water | P100(MWO)+P0+P80(MWO) | 20:00+stop and stir+12:00 |
| b-3 Farro(perlato) | 25g farro+75g water | P100(MWO)+P0+P80(MWO) | 15:00+stop and stir+2:00 |
|  | 50g farro +150g water | P100(MWO)+P0+P80(MWO) | 15:00+stop and stir+3:00 |
|  | 75g farro +225g water | P100(MWO)+P0+P80(MWO) | 15:00+stop and stir+4:00 |
|  | 100g farro +300g water | P100(MWO)+P0+P80(MWO) | 15:00+stop and stir+5:00 |
| b-4 Quinoa | 50g quinoa +100g water | P100(MWO)+P80(MWO) | 4:00+ 3:00 |
|  | 100g quino +200g water | P100(MWO)+P80(MWO) | 4:00+ 4:00 |
| A-7 DESSERTS |  |  |  |
| b-1 Cake | 300g | P100(MWO)+ P80(Grill) | 2:30+1:00 |
|  | 600g | P100(MWO)+ P80(Grill) | 4:00+1:30 |
| b-2 Biscuits | 250g | CO1+P80(Grill) | 4:00+1:30 |
| b-3 Muffins | 250g | P100(MWO)+ P80(Grill) | 2:00+1:00 |
|  | 500g | P100(MWO)+ P80(Grill) | 3:00+1:00 |
| b-4 Jam | 300g | P100(MWO)+P0+ P100(MWO) | 8:00+stop and mix+8:00 |
|  | 600g | P100(MWO)+P0+P100(MWO) | 10:00+stop and mix+10:00 |
| A-8 POTATOES/ROOT VEGETABLES |  |  |  |
| b-1 Baked sweet potatoes | 350g | P100(MWO)+P0+ P100(MWO) | 4:00+stop and mix+2:30 |
|  | 700g | P100(MWO)+P0+ P100(MWO) | 5:00+stop and mix+4:00 |
| b-2 Baked potatoes | 250g | CO2+P0+CO2+P80(Grill) | 12:00+stop and mix+12:00+10:00 |
|  | 500g | CO2+P0+CO2+P80(Grill) | 15:00+stop and mix+15:00+10:00 |
| b-3 Boiled potatoes | 250g | P100(MWO)+P0+ P100(MWO) | 6:00+stop and mix+3:30 |
|  | 500g | P100(MWO)+P0+ P100(MWO) | 6:00+stop and mix+5:00 |
| b-4 Beetroots | 250g+50ml water | P100(MWO) | 8:00 |
|  | 500g+70ml water | P100(MWO) | 9:30 |

PRESET FUNCTION

This function allows you to start a cooking program at an appointed time as you like.

- Set a cooking program.

- Touch  pad.

- Press “+ -” pad to set the hour digit

- Press START to confirm

- Press “+ -” pad to set the minute digit.

- Press START to confirm

Note: Before using the function, please confirm the oven clock time is correct. During presetting time, you can check the appointed time by pressing  pad, and cancel this program by pressing  pad and Stop pad.. QUICK START and DEFROST function can not set be preset.

OTHER CONVENIENT FEATURES

ECO MODE

Method :press the "" button, the buzzer sends out" DE ", display is light off.

Lifting method : press any button, the buzzer sends out" DE ", the system restores the original.

SLIENCE

Method : In standby, press the "" button, the buzzer sends out" DE ", mute function has been opened, this time by all the function keys have no "DEDE" prompt tone.

Lifting method : press the "" button, the buzzer sends out" DE ", mute function is closed, the system restores the original.

CHILD PROOF LOCK

The child proof lock prevents unsupervised operation by little children.

To set the child proof lock: In standby mode, press  button for 3 seconds, then a beep will sound and the indicator light will on. In the lock state, all buttons are disabled.

To cancel the child proof lock: Press  button for 3 seconds, then a beep will sound and the indicator light will off.

TO STOP THE OVEN WHILE THE OVEN IS OPERATING

- Press STOP button.

You can restart the oven by pressing START pad.

Touch STOP twice to erase all instructions.

2. Open the door.

You can restart the oven by closing the door and pressing START pad.

NOTE: Oven stops operating when door is opened.

OVERHEATING PROTECTION

When the system enters into super high temperature protection status, the digital display shows “E01” and continues to beep till the system comes back to normal condition and then press “STOP”.

LOW-TEMPERATURE PROTECTION

When the system enters into super low temperature protection status, the digital display shows “E02” and continues to beep till the system comes back to normal condition and then press “STOP”.

SENSOR MALFUNCTION PROTECTION

The system enters into protection mode when the system sensor is Short Circuited. The display shows “E03” and continues to beep until pressing “STOP” button. Call consumer service to check and replace the faulty sensor.

COOLING FEATURE

The electronically controlling system of the microwave oven has the feature of cooling. As for any cooking mode which cooking time above 2 minutes, after finishing cooking, the oven fan will work about 3 minutes automatically to cool the oven for prolonging the life of the oven.

AUTO REMINDER

After cooking or defrost program, beeps sound and END appears in display. Touch any button or open oven door to clear END before starting another cooking function.

By placing the      marking on this product, we declare, on our own responsibility, compliance to all of European safety, health and environmental requirements stated in the legislation for this product .

# CLEANING AND CARE

- Turn off the oven and remove the power plug from the wall socket before cleaning.

- Keep the inside of the oven clean. When food splatters or spilled liquids adhere to oven walls, wipe with a damp cloth. Mild detergent may be used if the oven gets very dirty. Avoid the use of spray and other harsh cleaners as they may stain, streak or dull the door surface.

- The outside surfaces should be cleaned with a damp cloth. To prevent damage to the operating parts inside the oven, water should not be allowed to seep into the ventilation openings.

- Wipe the door and window on both sides, the door seals and adjacent parts frequently with a damp cloth to remove any spills or spatters. Do not use abrasive cleaner.

- Do not allow the control panel to become wet. Clean with a soft, damp cloth. When cleaning the control panel, leave oven door open to prevent oven from accidentally turning on.

- If steam accumulates inside or around the outside of the oven door, wipe with a soft cloth. This may occur when the microwave oven is operated under high humidity condition. And it is normal.

- It is occasionally necessary to remove the glass tray for cleaning. Wash the tray in warm sudsy water or in a dishwasher.

- The roller ring and oven floor should be cleaned regularly to avoid excessive noise. Simply wipe the bottom surface of the oven with mild detergent. The roller ring may be washed in mild sudsy water or dishwasher. When removing the roller ring from cavity floor for cleaning, be sure to replace in the proper position.

- Remove odors from your oven by combining a cup of water with the juice and skin of one lemon in a deep microwaveable bowl, microwave for 5 minutes. Wipe thoroughly and dry with a soft cloth.

- When it becomes necessary to replace the oven light, please consult a dealer to have it replaced.

- The oven should be cleaned regularly and any food deposits removed. Failure to maintain the oven in a clean condition could lead to deterioration of the surface that could adversely affect the life of the appliance and possibly result in a hazardous situation.

- Please do not dispose this appliance into the domestic rubbish bin, it should be disposed to the particular disposal center provided by the municipalities.

- When the microwave oven with grill function is first used, it may produce slight smoke and smell. This is a normal phenomenon, because the oven is made of a steel plate coated with lubricating oil, and the new oven will produce fumes and odor generated by burning the lubricating oil. This phenomenon will disappear after a period of using.

# Text boxes

Please read these instructions carefully before installing and operating the oven.

Record in the space below the SERIAL NO. found on the nameplate on your oven and retain this information for future reference.

SERIAL NO.